## Slide 1
cFS hides the OS and the hardware behind layered APIs, and its apps talk over a software bus
Architecture brief on NASA’s core Flight System (cFS), documented from NASA’s public materials, 2015 to 2023.
Context
NASA’s Goddard Space Flight Center created cFS [2, p2], and its Flight Software Systems Branch maintains it as open source under Apache 2.0 [4]. NASA defines it as “a platform and project independent reusable software framework and set of reusable software applications” [1, p7]. Current code and docs: github.com/nasa/cFS, release v7.0.1 as of Oct. 6, 2026 [4].
What each layer hides from the one above
Layer | What NASA says it provides | What the layer above does not see
cFE services: ES, SB, EVS, TIME, TBL | “services that are common to most flight applications” [1, p25, p45] | OS task services, behind ES [1, p61], and who receives a message [1, p85]
OSAL | One API to the cFE “regardless of the underlying real-time operating system” [1, p23] | Which real-time OS runs underneath
PSP | One API “to underlying avionics hardware and board support package” [1, p24] | The board and its support package
RTOS and boot | The “software interface between the processor and the FSW” [1, p22] | The processor
NASA’s rule for every layer: “Each layer ‘hides’ its implementation and technology details.” [3, slide 8]
One housekeeping packet, six steps across the software bus
Flight software, one processor
Scheduler app (SCH)
Sending app
Telemetry Output app (TO)
Ground system
pipe
pipe
Software bus (cFE SB)
routes each message ID to every subscribed pipe
UDP/IP
1
2
2
3
4
5
6
1
Subscribe. At startup, TO creates a pipe and subscribes it to the packet’s ID [1, p85, p93].
2
Request. The Scheduler app sends a housekeeping request over the bus [1, p86, p34].
3
Build. The app fills its packet and stamps the time in the header [1, p88, p98].
4
Send. The app sends it on the bus without knowing who subscribes [1, p85, p97].
5
Route. The bus delivers it to every pipe subscribed to its ID [1, p85].
6
Downlink. TO reads its pipe and sends the packet over UDP/IP [1, p95, p34].
2021 names: CFE_SB_SendMsg, CFE_SB_RcvMsg [1, p97]. Current guide: CFE_SB_TransmitMsg, CFE_SB_ReceiveBuffer [5, 6.6, 6.7].
Tradeoffs NASA states
•
Copies slow large messages. Each send copies the message into a bus buffer, which NASA calls a “drawback” [5, 6.8].
•
A full pipe rejects new messages, so one slow app cannot hold up routing to the others [5, 6.1.2.1].
•
A reset clears the bus. “Any packet in transit at the time of the reset is discarded” [1, p90].
•
The abstraction has edges. Time design “is tightly coupled with the mission avionics design” [1, p129], and on GPM the “Addition of PSP changed build infrastructure midstream” [2, p14].
•
The open bundle is a starting point. It “has not been fully verified as an operational system” [4].
[1] NASA/TM-20205000691/REV 1, "Core Flight System (cFS) Training," NASA Goddard, Jan. 2021, NTRS 20205011588 (printed pages).
[2] McComas et al., "Core Flight System (cFS) a Low Cost Solution for SmallSats," NASA Goddard, Aug. 2015, NTRS 20150018075.
[3] Baker, "core Flight System (cFS) Overview," NASA Goddard, 2023, NTRS 20230002444. [4] nasa/cFS README, read Oct. 6, 2026.
[5] "cFE Application Developers Guide," nasa/cFE docs on GitHub, read Oct. 6, 2026 (section numbers).
Portfolio brief drawn from public NASA documents. Not a NASA document.