## Slide 1
One housekeeping packet crosses the software bus in six steps, and the app that sends it does not know who subscribed
Flight software, one processor
Scheduler app (SCH)
Sending app
Telemetry Output app (TO)
Ground system
pipe
pipe
Software bus (cFE SB)
routes each message ID to every subscribed pipe
Other subscribers, such as Data Storage
UDP/IP
1
2
2
3
4
5
5
6
1
Subscribe. At startup, TO subscribes a pipe to the packet’s ID.
2021 memo, p85 and p93
2
Request. The scheduler sends a housekeeping request over the bus.
2021 memo, p86 and p34
3
Build. The app fills its housekeeping packet and stamps the time.
2021 memo, p88 and p98
4
Send. The app sends the packet without knowing who subscribes.
2021 memo, p85 and p97
5
Route. The bus routes it to every pipe subscribed to its ID.
2021 memo, p85
6
Downlink. TO reads its pipe and sends the packet over UDP/IP.
2021 memo, p95 and p34
Sources: steps from NASA/TM-20205000691/REV 1 (the 2021 memo), Jan. 2021, NTRS 20205011588, printed pages. TO in the open-source bundle is a lab app meant as an example (nasa/cFS README). The memo’s CFE_SB_SendMsg and CFE_SB_RcvMsg (p97) are CFE_SB_TransmitMsg and CFE_SB_ReceiveBuffer in the current cFE Application Developers Guide (nasa/cFE, sec. 6.6 and 6.7, read Oct. 6, 2026).
Portfolio diagram drawn from public NASA documents. Not a NASA document.